BOLLARDS

Description.  This item shall consist of furnishing and placing metal bollards per the details and layout on the plans.

Materials.   See attached specifications.

CONSTRUCTION REQUIREMENTS

General.  See the following specification – BOLLARDS

BOLLARDS

GENERAL

SUMMARY

Section Includes:

Decorative or protective metal bollards.

Mounting hardware (concrete and anchors by others)

Edit following to coordinate with other specification sections in project.

REFERENCE STANDARDS

ASTM D1654 – Standard Test Method for Evaluation of Painted or Coated Specimens Subjected to Corrosive Environments.

SUBMITTALS

Product Data: Provide for each type of bollard, component, finish, and accessory specified.

Color Samples: Submit manufacturer’s standard. Setting Drawings: Show embedded items and cutouts required for work specified in other Sections.

Maintenance Data: Submit manufacturer’s field touch-up, cleaning, and maintenance instructions.

Warranty Documentation: Submit sample of manufacturer’s warranty.

DELIVERY, STORAGE AND HANDLING

Protect bollards and accessories during delivery, storage, and handling to comply with manufacturer’s instructions and prevent damage.

WARRANTY

Provide manufacturer’s one-year warranty agreeing to repair or replace components with manufacturing defects.

PRODUCTS

MANUFACTURERS

Acceptable Manufacturer:

Architectural Iron Company, phone 800-442-4766, fax 570-296-4766, website

www.architecturaliron.com or www.americanbollard.com email info@architecturaliron.com

Aluminum weighs less than cast iron, an especially important consideration for removable bollards. When its finish coat is damaged, aluminum oxidizes a color that is generally more acceptable than the red rust produced by cast iron.

MATERIALS

Gray iron castings: ASTM A48 Class 30 Gray Iron, ASTM A500 Schedule 40 pipe

See Reliance Foundry website or product literature for CAD details and additional information about various styles. Contact manufacturer for assistance with customized designs. Image of specified styles may be retained below or inserted into Drawings.

BOLLARDS

A.	Model AIC-957-958RL

Model AIC-957-958RL Garden City “C” Removable/Lockable Bollard:

Size: 36 inches high x 8 5/8 inches diameter.

Design: Cylindrical with base and cap – removable/removable.

Material: Gray iron castings: ASTM A48 Class 30 Gray Iron.

Steel: ASTM A500 Steel

FINISH

Primer: Sherwin Williams Kem-Bond HS Universal Metal Primer, Red Oxide B50NZ3 630-4521 (factory applied).

Recommend Finish Paint: Sherwin Williams Sher-Kem High Gloss Metal Finishing Enamel, Raven Black F75BC14 6016-49403 (not factory applied).

Performance: 1000 hours salt-spray resistance when in accordance with ASTM D1654.

Bollards can be installed in new construction or on existing surfaces. Coordinate installation hardware requirements with manufacturer based on installation type for direct burial installation.

INSTALLATION HARDWARE

Provide for standard direct burial installation where shown on the plans as directed by architect or engineer.

Retain following if required. Show locations where chain is required, quick-release locations, and drape of chain.

EXECUTION

EXAMINATION

Examine paving or other substrates for compliance with project architect or engineers requirements for placement and location of embedded items, condition of substrate, and other conditions affecting installation of bollards.

Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

General: Comply with manufacturer’s installation requirements and setting plans for direct burial installation or as directed by project specifications.

Damaged, cracked, chipped, deformed or marred bollards are not acceptable. Field touch-up minor imperfections in accordance with manufacturer’s instructions.

CLEANING & PROTECTION

Protect bollards against damage.

Immediately prior to Substantial Completion, clean bollards in accordance with manufacturer’s instructions to remove dust, dirt, adhesives, and other foreign materials.

CLOSEOUT ACTIVITIES

Provide maintenance information to Owner’s representative.

Provide warranty paperwork to Owner’s representative.

END OF SECTION

Method of Measurement.  This work will be measured for payment in units of each.

Basis of Payment. This work shall be paid for at the contract unit price per each for BOLLARDS, which price shall include all material specified on the detail.